## Slide 1: HAL-Funktionen

## Slide 2: GPIO-Steuerung
void
HAL_GPIO_WritePin(GPIO_TypeDef* GPIOx,
uint16_t GPIO_Pin,
GPIO_PinState PinState)
void
HAL_GPIO_TogglePin(GPIO_TypeDef* GPIOx, uint16_t GPIO_Pin)
GPIO_PinState
HAL_GPIO_ReadPin(GPIO_TypeDef* GPIOx, uint16_t GPIO_Pin)

## Slide 3: Timer und PWM-Steuerung
HAL_StatusTypeDef
HAL_TIM_PWM_Start(TIM_HandleTypeDef* htim,
uint32_t Channel)
HAL_StatusTypeDef
HAL_TIM_PWM_Stop(TIM_HandleTypeDef* htim, uint32_t Channel);

## Slide 4: Timer und One-Pulse-Steuerung
HAL_StatusTypeDef
HAL_TIM_OnePulse_Start(TIM_HandleTypeDef* htim,
uint32_t OutputChannel)

## Slide 5: SPI-Funktionen
HAL_StatusTypeDef
HAL_SPI_TransmitReceive(SPI_HandleTypeDef* hspi,
uint8_t* pTxData,
uint8_t* pRxData,
uint16_t Size,
uint32_t Timeout)
-> Transmit and Receive an amount of data in blocking mode. The CPU handles the timeout by actively polling the time and the state of the SPI Peripheral

## Slide 6: FreeRTOS-Funktionen

## Slide 7: Task Creation
BaseType_t xTaskCreate( TaskFunction_t pvTaskCode,
const char * const pcName,
const configSTACK_DEPTH_TYPE uxStackDepth,
void *pvParameters,
UBaseType_t uxPriority,
TaskHandle_t *pxCreatedTask
);

## Slide 8: Flow Control
void vTaskDelay( const TickType_t xTicksToDelay );
void vTaskSuspendAll( void );
BaseType_t xTaskResumeAll( void );

## Slide 9: Queue Control
QueueHandle_t xQueueCreate( UBaseType_t uxQueueLength,
UBaseType_t uxItemSize );
BaseType_t xQueueSend( QueueHandle_t xQueue,
const void * pvItemToQueue,
TickType_t xTicksToWait
);

## Slide 10: Queue Control
BaseType_t xQueueReceive( QueueHandle_t xQueue,
void *pvBuffer,
TickType_t xTicksToWait
);
BaseType_t xQueueSendFromISR( QueueHandle_t xQueue,
const void *pvItemToQueue,
BaseType_t *pxHigherPriorityTaskWoken
);

## Slide 11: Mutex and Semaphores
SemaphoreHandle_t xSemaphoreCreateBinary( void )
SemaphoreHandle_t xSemaphoreCreateMutex( void )
xSemaphoreGive( SemaphoreHandle_t xSemaphore );
xSemaphoreTake( SemaphoreHandle_t xSemaphore,
TickType_t xTicksToWait );

## Slide 12: Timer Functions
TimerHandle_t xTimerCreate( const char * const pcTimerName,
const TickType_t xTimerPeriod,
const UBaseType_t uxAutoReload,
void * const pvTimerID,
TimerCallbackFunction_t pxCallbackFunction );